Functional Specification for GUI
GUI version of QTDSP spectrum analyzer

The sim folder of the QTDSP paper contains a C99 console app to convert an input file of data (in ASCII format at one point per line) to a BMP file.

The GUI version of the application renders the BMP. The BMP is very wide, so a scroll bar and scroll buttons need to be able to pan across it. The C99 app converts the input file to a horizontal row of pixels, one row at a time. The algorithm needs to be modified to build the BMP in vertical stripes. This requires saving intermediate results between stripe calculations. The stripes can be built as needed rather than processing the entire input stream before displaying something. It’s also needed if the input stream in real-time instead of coming in from a file. If there is an input stream, such as from a digitizer, it should be saved to a file for future playback.

The GUI should use a GPU for processing the FFT. CUDA or OpenCL can be used. CUDA looks easier to use. It integrates into Visual Studio but uses OpenGL for graphics. The app could start without a GPU by using FFTW3, which is GPL-licensed. Since the GUI project is going to be open-source, it’s okay to develop under GPL. The GUI could be based on an OpenGL framework, but Win32 or Xamarin could be used.

The C99 version has its parameters adjustable on the command line. The GUI version uses various controls or menu items to set parameters. A data stream is converted to a 2D image and then to a BMP. Some parameter changes require a complete recalculation. Height and width are determined by the graphical area of the GUI, so they aren’t programmable.

The following controls determine the shading of the bitmap, so they don’t change the image data.

Parameter	Type	Control Usage / range
Auto	Button	Set fields to best guess
Floor	Slider	Numeric text box, dB level of “cold” color
Ceiling	Slider	Numeric text box, dB level of “hot” color
Scheme	RadioButton or Menu	BMP color scheme: B/W, color.
Filter	Checkbox	Enables filter, which doesn’t currently work in the C99 version

The following controls affect creation of the bitmap, so re-computation afterwards takes longer.

Parameter	Type	Control Usage / range
Data Source	EditText	Filename or stream setup
m	Dropdown	Decimation factor for downsampling
N	Dropdown	Set new N, must be a power of 2 between 128 and 16384
x	Dropdown	Set new X step size, range 4 to N
g	EditText	Set new gamma, range 0.001 to 1.0
Rmin	Slider	Minimum R value
Rmax	Slider	Maximum R value