Functional Specification for GUI
GUI version of QTDSP spectrum analyzer

The sim folder of the QTDSP paper contains a C99 console app to convert an input file of data (in ASCII format at one point per line) to a BMP file.

The GUI version of the application should use a GPU for processing the FFT. CUDA or OpenCL can be used. CUDA looks easier to use. The app could start without a GPU. It can use FFTW3, which is GPL-licensed. Since the GUI project is going to be open-source, it’s okay to develop under GPL. The GUI should be based on an OpenGL framework.

The C99 version has its parameters adjustable on the command line. The GUI version uses various controls or menu items to set parameters. A data stream is converted to a 2D image and then to a BMP. The following controls determine the shading of the bitmap, so they should be the most accessible.

Parameter	Type	Control Usage	Range
Auto	Button	Set fields to best guess
Floor	Slider	Numeric text box, dB level of “cold” color
Ceiling	Slider	Numeric text box, dB level of “hot” color

- -b <filename> Set bmp output filename
- -i <filename> Set input filename
- -m Set new decimation factor, range = 1 to 100
- -o Set offset to starting point in file, must be >=0
- -N Set new N, must be a power of 2 between 128 and 16384
- -r Set new Rmin
- -R Set new Rmax
- -g Set new gamma, range 0.001 to 1.0
- -x Set new X step size, range 4 to N
- -f Set floor of heatmap
- -c Set ceiling of heatmap
- -h Set BMP height to multiple of 4
- -w Set BMP width
- -v Set verbose mode: dumps extra stuff
- -a Enable autowidth
- -F Set floor relative to ceiling in dB
- -M Set color scheme to monochrome
- -z Enable extra filtering (not working)